## Slide 1: Exercise 1
Safety & Basic Skills

## Slide 2: Laboratory Safety
Bacteria:
  Wear gloves
  Wash your hands after removing gloves
  Notify TAs of spills or contamination
Chemicals:
  Always handle reagents with caution
UV Light:
  Never look at UV lamps
  Wear protective gloves to protect your own skin cells from UV damage

## Slide 3: Lab Safety Importance
Working with chemicals &equipment can have consequences now and in the future
  Toxic or infectious substances could result in acute or chronic illness or even death.
  Explosions or fires can injure or kill.
Knowledge of safety is critical in protecting yourself and others from potential hazards.

## Slide 4: Housekeeping
To avoid accidental ingestion of toxic or infectious materials, the following are prohibited in the lab:
  Eating or drinking
  Taking medication
  Applying lip balm, gloss, lipstick or make-up

## Slide 5: Hand Hygiene
Wearing gloves is the best way to keep your hands free of chemicals/reagents/bacteria
When choosing gloves:
  Make sure to choose gloves that are the appropriate size and fit well
  Do not use gloves that have holes or cracks
  Always remove gloves before leaving the room
  Remove gloves by pulling cuff down over your hand, turning the glove inside out
  Never touch door knobs or handles with gloved hands
Always wash hands after removing gloves

## Slide 6: Personal Protective Equipment (PPE)
PPE items in the lab can include:
  Lab Coats
  Goggles
  Gloves
  Fully enclosed footwear
  Clothing the covers legs (long pants) and midriffs
  Respiratory protection

## Slide 7: Biosafety Levels
Biosafety is the application of a combination of laboratory practices and procedures, laboratory facilities, and safety equipment when working with biological material
Biosafety levels:
  BL1 - Agents not known to cause disease consistently in healthy humans
  BL2 - Agents associated with human or animal disease
  BL3 - Indigenous/exotic agents associated with human or animal disease and with potential for aerosol transmission
  BL4 - Dangerous/exotic agents of life threatening nature

## Slide 8: Sharps
The Illinois EPA defines sharps as:
  Any medical needle
  Syringe, with or without needle
  Scalpel and razor blade
  Blood vials
  Pasteur pipets
  Microscope slides and coverslips
  Glassware contaminated with infectious agents
Sharps must be disposed of in approved Sharps container

## Slide 9: Biological Waste
Cultures, stocks and disposable labware generated from experiments with biological materials must be autoclaved prior to disposal
  Place these materials, as directed, into red biological waste disposal bags in the lab
  Do NOT put these materials into regular trash
  If you are uncertain, please ask!

## Slide 10: Emergency Preparedness
Students should be aware of the safety measures around the lab for their protection. These would include:
  Safety Shower
  Eyewash Station
  Fire extinguisher
  Spill kit
  Nearest exit

## Slide 11: Fire Safety
If fire occurs:
  Notify those in the immediate area
  Activate nearest fire alarm
  Confine the fire by closing doors and windows
  Attempt to extinguish the fire only if it is safe to do so
  Do not use elevators
  If possible, call 911 to explain the nature of the fire or emergency and meet responders outside

## Slide 12: DRS
The DRS website provides campus-specific safety information such as:
  Safety guidance documents in the "Safety Library”
  Online Safety Trainings
  Information on how to manage hazardous waste
  Information on DRS safety programs
  Accident response information
  Templates and forms for managing hazards in the laboratory

## Slide 13: Exercise 1B: Basic Laboratory Skills
,

## Slide 14: Goals
Understand and manipulate exponential numbers.
Become familiar with the units used for small concentrations and volumes and be able to make conversions between them.
Figure out concentrations of solutions or cell suspensions after dilution.
Understand what is meant by pH and know how to calculate the pH of a solution.
Understand how buffers work.

## Slide 15: Exponential Numbers
Every number can be expressed as the product of two numbers, the second one being some power of ten.
      For example, the number 100 can be expressed as 10 X 10 = 102
      The same rules are used to express numbers less than one.
    10-2 = 1/10 X 1/10 = 1/100

## Slide 16: Units of Measurement
    Common units
    Mass
    1 gram (g) = 103 milligrams (mg)
    = 106 micrograms (µg)
    = 109 nanograms (ng)
    Volume
    1 liter (l) = 103 milliliters (ml)
    = 106 microliters (µl)
    1 ml = 1 cubic centimeter
    Length
    1 meter (m) = 103 millimeters (mm)
    = 106 micrometers (µm)
    = 109 nanometers (nm)

## Slide 17: Dilutions
C1V1 = C2V2
Example: Given a 1 M stock solution of Tris buffer prepare 10 ml of 0.01 M Tris.
Solution: The question you need to answer is "what volume of 1 M Tris do you need to dilute to give a total volume of 10 ml of 0.01 M Tris". Thus, you know C1, C2, and V2.
(? ml x 1 M) = (10 ml x 0.01 M)
? ml = 10 ml x 0.01 M
(1 M)
Answer: 0.1 ml

## Slide 18: Dilution Factor
Dilution = 1/100 Dilution Factor: 100
Dilution = 1/n Dilution Factor: n
Serial Dilution: product of the individual dilutions
1/102 x 1/10 x 1/103 = 1/106 = 10-6

## Slide 19: Aqueous Solutions
An aqueous solution is one in which water is the solvent.
Water properties:
High surface tension
High boiling point
Good Solvent

## Slide 20: Acids, Bases, pH and Buffer
Acids/Bases:
Bronsted Definition: an acid is a molecule that donates protons and a base is a molecule that accepts protons
pH:
Dependent upon the concentrations of H+ and OH- ions
Buffers:
A molecule that allows the solutions to resist changes in the hydrogen ion concentration

## Slide 21: Mini Quiz 2
Friday, February 12
Students will take Mini Quiz 2 in Compass
The Mini Quiz will be open for 12 hours (9 AM – 9 PM CST)
Once you begin the quiz, you will have 15 minutes to complete it
Mini Quiz 2 covers:
  Materials for this quiz were drawn from manual pages 1-22
  Videos in the Lab 1: Safety & Basic Skills folder in Compass